## Slide 1
Automated PCB Defect Detection System
Name : D.Sritha

## Slide 2
Objective : Precision in PCB Inspection
This project aims to eliminate inefficiencies in manual PCB quality inspection by implementing an end-to-end AI-powered defect detection and classification pipeline. The system automates defect identification using advanced image processing and deep learning techniques, significantly reducing inspection time and human error. High-accuracy defect classification is achieved using the EfficientNet-B0 architecture, capable of identifying six critical PCB defects .
1
2

## Slide 3
System Architecture
1
Dataset Setup & Image Subtraction
2
Contour Detection & ROI Extraction
3
CNN Model Training (EfficientNet-B0)
4
Inference Pipeline & Prediction
5
Web Frontend (Streamlit UI)
6
Backend Integration
7
Performance Analytics & Export

## Slide 4
Dataset Setup & Image Subtraction
Robust Template Matching Before defect detection, the system identifies the correct defect-free reference PCB from a library of golden templates. Normalized Cross-Correlation is used to compare the test image against each template, automatically selecting the best match with an average similarity score of 0.8744. To ensure reliable alignment, a minimum similarity threshold of 0.6 is enforced, preventing incorrect template selection and misregistration.
Intense Defect Extraction Pipeline Once alignment is achieved, a multi-stage computer vision pipeline is applied to extract defect regions by emphasizing differences between the test PCB and the matched template. CLAHE is used to normalize local contrast, ensuring defect visibility under varying illumination conditions. Adaptive thresholding with 11×11 local windows handles non-uniform reflections across the PCB surface. Median blur filtering removes salt-and-pepper noise while preserving sharp defect boundaries, and certainty masking applies a global threshold to suppress shadow artifacts and false positives.

## Slide 5
Contour Detection & ROI Extraction
Contour-Based Defect Localization
Noise Suppression
Bounding Box Extraction
Contextual Padding for CNNs
Defect Class Coverage
Scalability Result
Training Consistency
Precision Validation

## Slide 6
Model Architecture: EfficientNet-B0 pre-trained on ImageNet, fine-tuned for 6 PCB defect classes using a custom classification head.
Input Configuration: Defect ROIs resized to 128×128 pixels to balance spatial detail and computational efficiency.
Data Augmentation: Random flips, rotations, and slight color jitter applied during training to improve generalization and reduce overfitting.
Train–Validation Split: Dataset split into 80% training and 20% validation to ensure unbiased performance evaluation.
Optimization Strategy: Trained using Adam optimizer with cross-entropy loss and adaptive learning rate reduction based on validation loss.
Early Stopping: Training automatically stops when validation loss stops improving, preventing overfitting and saving the best model.
Performance Monitoring: Accuracy and loss tracked per epoch with learning curves for training stability analysis.
Final Evaluation: Model performance assessed using confusion matrix, precision, recall, and F1-score for each defect class.
CNN Model Training (EfficientNet-B0)

## Slide 7
Template Selection
  Automatically loads best-matching “Golden Reference” board
Mask Generation
  Isolates potential defect regions via image subtraction
ROI Extraction
  Detects contours and crops areas of interest for AI analysis
CNN Classification
  Cropped ROIs classified using EfficientNet-B0
Visualization
  Annotates original image with bounding boxes & defect labels
Performance Benchmarks
Average Latency: 0.847 sec/image (GPU)
Detection Rate: 97.3% true positive defects
False Positive Rate: 2.1%
Evidence Chain: Generates reference, mask & labelled predictions for verification
Inference Pipeline & Prediction

## Slide 8
Backend Pipeline: Robust & Efficient
Frontend (Streamlit)
File Upload Handler
Template Matcher → Image Processor → CNN Inference
Result Formatter
UI Renderer (Images + Dataframe)

## Slide 9
Live Inspection: Real-time processing results & visual feedback
Historical Trends: Tracks latency and detection trends over time
KPI Tracking: Average template match score & cumulative defect counts
Reduced Latency: 1.42s → 0.847s per image
Memory Efficiency: Peak memory optimized from 2.1GB → 1.3GB
Batch Processing: High-throughput at 5 images/sec
Data Export Capabilities in csv and images
Annotated Images: High-res JPGs with bounding boxes, labels & confidence
CSV Logs: Structured report with defect IDs, types, confidence & coordinates
Best Accuracy: ~99%
Training Progress: Rapid convergence, early stopping triggered at epoch 11
Stable Loss: Smooth reduction in training & validation loss
Performance Analytics & Export